## Slide 1: Basic troubleshooting for CRTs
Lack of improvement in HF symptoms or sudden deterioration in symptoms in patients with CRT
ECG
Rhythm
Sinus rhythm
AF/ A flutter
Rate control adequate?
Yes
No
Review rate control medications +/- need for AV node ablation
Paced ECG?
No
Yes
Check device settings – Base rate, Programmed A-V delay
Perform chest X-Ray to check lead position
Paced QRS morphology
LBBB (Negative R wave in V1)
Likely RV only pacing
RBBB (Dominant R wave in V1)
Likely Bi-V or LV only pacing
QRS duration
Broad
Consider device optimisation
Narrow
Consider rhythm control
If LV only pacing
Consider medication review/detailed device check +/-expert opinion if no obvious initial cause identified
Compare with post CRT implant ECGs (intrinsic QRS, RV/ LV and BiV paced) if available
S.Venkatasubramanian, Heart Failure Hub Scotland, Oct 2018

## Slide 2: Common Causes for Sub-optimal Bi-V Pacing
Lead issues
  Under/ over sensing
  Lead displacement
  Lack of capture
Programming issues
  Device base rate set lower than intrinsic HR
  Programmed A-V delay longer than sensed/ intrinsic A-V delay – allowing intrinsic conduction
Atrial arrhythmias
  Poor ventricular rate control
  Programmed base rate lower than intrinsic rate during AF/ flutter
Frequent ventricular ectopics
  Consider need for Holter monitor to determine VE burden
  Consider increasing device base rate to suppress VEs
  Optimise beta blockers (Amiodarone in extreme cases) if frequent ectopy
S.Venkatasubramanian, Heart Failure Hub Scotland, Oct 2018

## Slide 3: Ensure Optimal Medical Therapy in ALL patients with CRT
Can ACEi/ ARB be increased post CRT (if not on top dose and BP allows)?
Is patient suitable for switching to Sacubitril/ Valsartan in place of ACEi/ ARB?
Is patient on top dose beta-blocker with CRT in situ? (no risk of bradycardia) (NB: Consider Ivabradine if in sinus rhythm and heart rate control inadequate despite beta-blockade)
Is rate control adequate (resting HR <80/min) in patients with CRT in AF? – consider adding Digoxin to beta-blockers to improve rate control; consider referral for AV node ablation if rate control inadequate despite optimal rate control
S.Venkatasubramanian, Heart Failure Hub Scotland, Oct 2018